## Slide 1: Help Needed! 
Need volunteers for the following research topics:
Microscopy image processing using 3D de-convolution
  Translate from Matlab code to Python
  And use GPU to accelerate (not an FPGA project but can be later :-P)
Discrepancy diagnosis between on-FPGA execution and software simulation
  Know Vivado and Verilog

## Slide 2: L3: FPGA 101
Cong (Callie) Hao
callie.hao@ece.gatech.edu
Assistant Professor
ECE, Georgia Institute of Technology
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/

## Slide 3: FPGA: Field-Programmable Gate Array
FPGA: Field-Programmable Gate Array
  An integrated circuit designed to be configured by a customer or a designer after manufacturing (wikipedia)
Components in an FPGA Chip
  Programmable logic blocks
  Programmable interconnects
  Programmable I/Os

## Slide 4: FPGA Components
SRAM-based implementation is popular
Look-up Tables (LUT)
  Flip-flop (FF)
  Slices and CLBs (configurable logic block)
Block Memory (BRAM)
DSP Blocks
Interconnect and routing resource

## Slide 5: Look-up-Table (LUT)
A k-input LUT (k-LUT) can be configured to implement any k-input 1-output combinational logic
  Requires 2k SRAM bits
  Delay is independent of logic function
Simply speaking, FPGAs are made of individual logic blocks, each of which is composed of a flip flop (FF) and a Lookup Table (LUT).
Truth table
3-Input LUT
Look
up
Table
a
b
c
d
Flip
Flop
out
A simple FPGA logic block
SRAM bits
(configurable)

## Slide 6: Look-up-Table (LUT)
Larger LUTs can be composed by smaller LUTs
Example: Xilinx 7-series FPGAs
A 6-input LUT can be two 5-input LUTs with common inputs
  Any function of six variables or two independent functions of five variables

## Slide 7: Slice and Configurable Logic Block (CLB)
Hierarchical design
  Each slice (called BLE in early generations) can be composed of multiple LUTs
  Each CLB can be composed of multiple slices
Example: Xilinx 7-series FPGAs
  Each CLB has two slices
  Each slice contains four LUTs
Ahmed, E. and Rose, J., The effect of LUT and cluster size on deep-submicron FPGA performance and density. IEEE TVLSI, 2004

## Slide 8: Traditional Homogeneous FPGA Architecture
Logic
block
Switch
block
Routing track

## Slide 9: Modern Heterogeneous Programmable SoC
Island-style configurable mesh routing
Lots of dedicated components
  Memories/multipliers, I/Os, processors
  Specialization leads to higher performance and lower power
Figure source: embeddedrelated.com
Image source: Ronak, Bajaj, and Suhaib A. Fahmy. "Mapping for maximum performance on FPGA DSP blocks." IEEE TCAD

## Slide 10: Dedicated Block RAMs (BRAMs)
Block RAMs are used for storing large amounts of data inside of your FPGA
  They are SRAM
  Also called on-chip memory
  Typically, at most two ports
  Different ports can be accessed at the same time
  Different RAM blocks can be accessed at the same time
Example: Xilinx 18K/36K block RAMs
  32k x 1 to 512 x 72 in one 36K block
  Simple dual-port and true dual-port configurations

## Slide 11: Dedicated DSP Blocks
DSP: Built-in components for fast arithmetic operation optimized for DSP applications
  Essentially a multiply-accumulate core with many other features
  Fixed logic and connections, functionality may be configured using control signals at run time
  Much faster than LUT-based implementation (ASIC vs. LUT)
DSPs and BRAMs are usually the bottleneck resources for efficient FPGA design
  Larger parallelism, more DSPs and BRAMs

## Slide 12: Example: Xilinx DSP48E1
25x18 signed multiplier
48-bit add/subtract/accumulate
48-bit logic operations
SIMD operations (12/24 bit)
Pipeline registers for high speed

## Slide 13: Example: Xilinx DSP48E1 (SIMD Mode)
Four 12-Bit SIMD Adder Configuration

## Slide 14: Example: Xilinx DSP48E1
https://www.xilinx.com/support/documentation/user_guides/ug579-ultrascale-dsp.pdf

## Slide 15: FPGA Routing Architecture

## Slide 16: Embedded FPGA System-on-Chip
Programmable Logic (PL)
This is where you design your accelerator
LUTs, BRAM, FF, DSP
Processing System (PS)
Dual ARM Cortex-A9 + NEON
SIMD extension @600MHz~1GHz
Handles data movement (e.g., sending to and receiving data from PL) and peripherals (e.g., display, key-board)
Controls PL
Called Host Code
DRAM

## Slide 17: More Advanced Architectures – HBM
High Bandwidth Memory (HBM) on Xilinx FPGA
https://www.xilinx.com/developer/articles/maximizing-memory-bandwidth-with-vitis-and-xilinx-ultrascale-hbm-devices.html

## Slide 18: More Advanced Architectures – HBM
High Bandwidth Memory (HBM) on Xilinx FPGA
  A theoretical bandwidth up to 460GB/s:
    2 x HBM stacks
    Each stack has 16 Channels
    Each channel is 64-bits of Data (DQ) bits Data can be transferred up to 1800Mbps
    2x16x64x1800Mbps = 3.686Tb/s or 460GB/s
https://www.xilinx.com/support/documentation/ip_documentation/hbm/v1_0/pg276-axi-hbm.pdf

## Slide 19: More Advanced Architectures – HBM
High Bandwidth Memory (HBM) on Xilinx FPGA
https://www.xilinx.com/support/documentation/ip_documentation/hbm/v1_0/pg276-axi-hbm.pdf
Bank group interleave reduces latency
32 AXI ports
32 pseudo channels (PC)

## Slide 20: More Advanced Architectures – ACAP
Which architecture is best for which task?
  Scalar processing elements (e.g., CPUs) are very efficient at complex algorithms with diverse decision trees and a broad set of libraries
    But are limited in performance scaling.
  Vector processing elements (e.g., DSPs, GPUs) are more efficient at a narrower set of parallelizable compute functions
    But experience latency and efficiency penalties because of inflexible memory hierarchy.
  Programmable logic (e.g., FPGAs) can be precisely customized to a particular compute function, which makes them best at latency-critical real-time applications (e.g., automotive driver assist) and irregular data structures (e.g., genomic sequencing)
    But algorithmic changes have traditionally taken hours to compile versus minutes.
https://www.xilinx.com/support/documentation/white_papers/wp505-versal-acap.pdf

## Slide 21: More Advanced Architectures – ACAP
Which architecture is best for which task?
  Scalar processing elements (e.g., CPUs) are very efficient at complex algorithms with diverse decision trees and a broad set of libraries
    But are limited in performance scaling.
  Vector processing elements (e.g., DSPs, GPUs) are more efficient at a narrower set of parallelizable compute functions
    But experience latency and efficiency penalties because of inflexible memory hierarchy.
  Programmable logic (e.g., FPGAs) can be precisely customized to a particular compute function, which makes them best at latency-critical real-time applications (e.g., automotive driver assist) and irregular data structures (e.g., genomic sequencing)
    But algorithmic changes have traditionally taken hours to compile versus minutes.
https://www.xilinx.com/support/documentation/white_papers/wp505-versal-acap.pdf

## Slide 22: More Advanced Architectures – ACAP
Xilinx introduces heterogeneous adaptive compute architecture, ACAP, which integrates the three:
  Vector and scalar processing elements tightly coupled to programmable logic (PL)
  With a high-bandwidth network-on-chip (NoC)
  They insist that ACAP is not FPGA…
https://www.xilinx.com/support/documentation/white_papers/wp505-versal-acap.pdf

## Slide 23: More Advanced Architectures – ACAP
AI Engines

## Slide 24: Screenshot from Vivado
DSPs
SLICE
Structure of a SLICE
LUTs
FFs

## Slide 25: A Real FPGA Design

## Slide 26: Summary
Key components on FPGA:
  Look-up Table (LUT)
  Block RAM (BRAM)
  DSP
  Flip-flop (FF)
  Routing resources
More advanced FPGA technology
  High bandwidth memory (HBM)
  Adaptive computing acceleration platform (ACAP)