## Slide 1: Biofuels ISOCONVERSION Process November 2015
Chuck Red
cred@ara.com
850.914.3188
David M. Wadsworth
dmwad@chevron.com
973.893.3840

## Slide 2
Catalytic Hydrothermolysis
Supercritical water process converts fats, oils, and greases from plant oils, algae, and animal fats into a crude oil that contains the same molecular distribution of petroleum crude
2 Minutes
Converts fats oils and greases to crude oil
Hydrotreating
Saturates olefins & removes any residual oxygenates.
Non-precious metal
Catalysts and conventional hydrotreating
reactor
Fractionation
Produces finished fuels – diesel and jet fuel that meet petroleum specifications without blending, renewable chemicals, and naphtha
Conventional
Refinery Processes
Biofuels ISOCONVERSION Process
Converts industrial oil feedstocks, fats, and greases into 100% drop in fuels and renewable chemicals

## Slide 3: Feedstocks – Fats, Oils, and Greases
  Algal
  Brown Grease
  Camelina
  Canola
  Carinata
  Castor
  Distillers Corn
  Fatty Acid Distillate
  Jatropha
  Microbial
  Peanut
  Shae Butter
  Soybean
  Tall oil
  Tallow
  Tung
  Yellow Grease
  Biofuels ISOCONVERSION is feedstock agnostic – can process any triglyceride or fatty acid material
ARA’s Hydrothermal Cleanup removes virtually all inorganic material from challenging feedstocks

## Slide 4: Products
ReadiJet CHCJ-5 – Renewable JP-5 Jet Fuel for Shipboard Use
ReadiDiesel CHD-76 – Renewable
F-76 Marine Diesel
ReadiJet Jet-A
Renewable Naphtha
Products are pure hydrocarbons with the same boiling rate distribution and molecular makeup as their petroleum counterparts
Renewable Naphtha
Renewable Chemicals – High value by-products including renewable alkyl aromatics, paraffins, acids, fatty alcohols

## Slide 5
GC X GC
Gas Chromatograph – Each bubble represents a different compound.
ARA fuels have same compounds and boiling range distribution as their petroleum counterparts.
Red and Blue bubbles represent paraffin molecules.
Yellow and brown bubbles represent cycloparaffin molecules
Green and orange molecules represent aromatic molecules
Petroleum Jet Fuel
ReadiJet

## Slide 6
CHJ Test Results

## Slide 7
GC X GC
Gas Chromatograph – Each bubble represents a different compound and the size represents its prevalence.
ARA fuels have same compounds and boiling range distribution as their petroleum counterparts.
Red bubbles represent paraffin molecules.
Yellow bubbles represent cycloparaffin molecules
Green bubbles represent aromatic molecules
Petroleum Diesel
ReadiDiesel

## Slide 8: Test Facility – Panama City, FL

## Slide 9: Certification
ASTM Certification –
  ReadiJet is next in queue for Research Report review
  Jet Fuel – D7566 Annex Summer 2016
MILSPEC Certification –
  100% renewable, drop in, unblended, JP-5 and F-76 – End of 2016

## Slide 10: Commercialization
Focus on low quality waste fats and oils
4 licenses in place
First 2 projects in engineering
Construction in 2016

## Slide 11
Questions?